PS2 JIT compiler port from i386/32bit to x86_64 code

PCSX2 has 6 recompilers:
- Micro VU0	: Vector Unit 0 (Alternative recompiler SuperVU is less compatible)
- Micro VU1	: Vector Unit 1
- R5900-32	: EE RISC processor ("Emotion Engine")
- R3000A	: I/O processor
- VIF0 Unpack : Vector Unit Interface 0
- VIF1 Unpack : Vector Unit Interface 1

Terms/abbreviations:
- GS	Graphics Synthesizer
- SIMD	Single instruction, multiple data
- ABI	Application Binary Interface (e.g. Kernel to application), either 32-bit or 64-bit
- Abbreviations used in x86 or x86_64 op codes:
  - byte	(8 bit)	suffix b	Integer
  - word	(2 bytes)	suffix w	Integer
  - doubleword	(4 bytes)	suffix l	Integer
  - quadword	(8 bytes)	suffix q e.g.	movq	copies 8 bytes	Integer
  - octword	(16 bytes)	suffix o	Integer
  - suffix z: fill leading bits with zero, e.g. copy 1 byte into 2 byte register
  - suffix s: sign extend upper portion e.g. negative byte copied to word fills with ones
  - cwtl	convert word to doublword
  - cltq	convert doubleword to quadword
  - cqto	convert quodword to octoword
  - Floating point single	(S)	4 bytes
  - Floating point double	(D)	8 bytes
  - Imm:	‘immediate’ value (a constant) stored in the instruction itself
    [e.g. ADDI $1,D0]–The $ indicates the constant/immediate
- ALU	Arithmetic and Logic Unit (performs arithmetic operations like addition and subtraction along with logical operations AND, OR, etc.)

Notes:
- VC0 and VC1 recomilers are disabled in x86_64 version, check DISABLE_SVU. Also on other platforms. How does that affect the performance?
- All processors that support the x86_64 instruction set also support the x86/i386/i686 instruction set. If a processor can run 64-bit code, it can also run 32-bit code. Each process, however, must be homogeneous, so either 32-bit or 64-bit.
- When generating code for 64-bit platforms, the order of operations may be different compared to generating 32-bit code.
- x86_64 CPUs
  - have two modes of operation in Long Mode, a 64-bit mode and compatibility mode. In compatibility mode, the default address size is 32 bits.
  - still make available x87/MMX registers in 64-bit mode
  - provide full x86 16-bit and 32-bit instruction sets without intervening emulation

Central files:
- pcsx2/pcsx2/R5900.cpp: EE emulation
- common/src/x86emitter/x86emitter.cpp
Questions to resolve:
- Which instructions have to be ported?
- Where does the order of operations change?
- Which modules are affected?

Existing instruction sets on i386:

- MMX: a single instruction, multiple data (SIMD) instruction set
  - 57 instructions
  - 64-bit wide register file (MM0-MM7)
  - only integer operations
  - not able to mix integer-SIMD ops with any floating-point ops
- SSE1: Streaming SIMD Extension 1
  - 128-bit wide register file (XMM0–XMM7)
- SSE2: Streaming SIMD Extensions 2
- SSSE3: Supplemental Streaming SIMD Extensions 3
- SSE4: Streaming SIMD Extensions 2
- AVX:	Floating Point
  - Advanced Vector Extensions (since 2011). AVX provides new features, new instructions and a new coding scheme.
  - AVX uses sixteen YMM registers to perform a Single Instruction on Multiple pieces of Data (see SIMD).
  - The AVX instructions support both 128-bit and 256-bit SIMD
  - Each YMM register can hold and do simultaneous operations (math) on:
    - eight 32-bit single-precision floating point numbers or
    - four 64-bit double-precision floating point numbers.
- AVX2 expands most integer commands to 256 bits and introduces fused multiply-accumulate (FMA) operations
Primary opcode maps:	(Escape sequences allow for different maps)
http://sparksandflames.com/files/x86InstructionChart.html

Registers on x86_64:

8-byte register	Byte 3-0	Byte 1-0	Byte 0
rax	Eax	ax	al
rcx	ecx	cx	cl
rdx	edx	dx	dl
rbx	ebx	bx	bl
rsi	esi	si	sil
rdi	edi	di	dil
rsp	esp	sp	spl
rbp	ebp	bp	bpl
r8	r8d	r8w	r8b
r9	r9d	r9w	r9b
r10	r10d	r10w	r10b
r11	r11d	r11w	r11b
r12	r12d	r12w	r12b
r13	r13d	r13w	r13b
r14	r14d	r14w	r14b
r15	r15d	r15w	r15b

Instruction encoding on AMD64: